Present and Future Regimes and Applications
of Laser-Plasma Ion Acceleration
Andrea Macchi
polyLAB, CNR-INFM, Pisa
Dipartimento di Fisica “Enrico Fermi”, Università di Pisa
and INFN, sezione di Pisa, Italy
CNR-IPCF, Pisa, December 6, 2007

---
Outline
The “new era” of laser acceleration of ions (mainly protons): their discovery and (foreseen) applications
Present regimes (mainly Target Normal Sheath Acceleration)
Future regimes (mainly Radiation Pressure Acceleration)
A proposal: RPA with circularly polarized pulses
Some (preliminary) suggestions for FLAME experiments

---
The discovery of MeV proton emission
in superintense interaction with metallic targets
Reported in 2000
by three experimental groups
[Clark et al, PRL 84 (2000) 670;
Maksimchuk et al, ibid., 4108;
Snavely et al, PRL 85 (2000) 2945 (*)]
- high number (up to 1014)
- good collimation
- ultra-low emittance (4 x 10-3 mm mrad)
- maximum energy and efficiency
  observed (*):
   58 MeV , 12% of laser energy
   @ I=3 x 1020 W/cm2
Remarkable properties
of the proton beam:

---
The discovery of MeV proton emission
in superintense interaction with metallic targets
Reported in 2000
by three experimental groups
[Clark et al, PRL 84 (2000) 670;
Maksimchuk et al, ibid., 4108;
Snavely et al, PRL 85 (2000) 2945 (*)]
- high number (up to 1014)
- good collimation
- ultra-low emittance (4 x 10-3 mm mrad)
- maximum energy and efficiency
  observed (*):
   58 MeV , 12% of laser energy
   @ I=3 x 1020 W/cm2
Question: why protons
from metallic targets?
Answer: presence of a layer
of hydrocarbon or water
impurities on
the target surface
Remarkable properties
of the proton beam:

---
The discovery of MeV proton emission
in superintense interaction with metallic targets
Reported in 2000
by three experimental groups
[Clark et al, PRL 84 (2000) 670;
Maksimchuk et al, ibid., 4108;
Snavely et al, PRL 85 (2000) 2945 (*)]
More debated question: are protons coming from the front or from the rear side?
i.e. what is the acceleration mechanism?
- high number (up to 1014)
- good collimation
- ultra-low emittance (4 x 10-3 mm mrad)
- maximum energy and efficiency
  observed (*):
   58 MeV , 12% of laser energy
   @ I=3 x 1020 W/cm2
Remarkable properties
of the proton beam:

---
MeV protons (ions) are appealing for applications
requiring localized energy deposition in matter
Sharp spatial maximum of
deposited energy
(Bragg peak)
Peak location depends
on energy
[U. Amaldi & G. Kraft, Rep. Prog. Phys. 68 (2005) 1861]

---
MeV protons (ions) are appealing for applications
requiring localized energy deposition in matter
Medical Applications
ONCOLOGICAL HADRONTHERAPY
[K.Ledingham, Glasgow University, 2006]
If feasible with table-top, high repetition lasers,
cost can be reduced with respect to an accelerator facility
Other foreseen application in medicine:
isotope production (e.g. for Proton Emission Tomography)

---
MeV protons (ions) are appealing for applications
requiring localized energy deposition in matter
Inertial Confinement Nuclear Fusion
FAST IGNITION
Protons can be used to create
a “spark” in a pre-compressed
ICF capsule achieving isochoric
burn and high energy gain
[Roth et al, Phys. Rev. Lett. 86 (2001) 436;
 Atzeni et al, Nuclear Fusion 42 (2002) L1;
 Macchi et al, Nuclear Fusion 43 (2003) 362]
Geometrical focusing of laser-accelerated protons and
localized isochoric heating
has been demonstrated
[Patel et al, Phys. Rev. Lett. 91 (2003) 125004]

---
Fast ions seen in PIC simulations suggest
several possible mechanisms of ion acceleration
1D PIC simulation
I=3.5×1020W/cm2 ,
ne=1022cm-3
Three fast ion populations,
accelerated
- from rear side
  in forward direction
- from front side
  in forward direction
- from front side
  in backward direction
Which is the dominant “channel” for given conditions?

---
Fast ions seen in PIC simulations suggest
several possible mechanisms of ion acceleration
1D PIC simulation
I=3.5×1020W/cm2 ,
ne=1022cm-3
Three fast ion populations,
accelerated
- from rear side
  in forward direction
- from front side
  in forward direction
- from front side
  in backward direction
Which is the dominant “channel” for given conditions?

---
Fast ions seen in PIC simulations suggest
several possible mechanisms of ion acceleration
1D PIC simulation
I=3.5×1020W/cm2 ,
ne=1022cm-3
Three fast ion populations,
accelerated
- from rear side
  in forward direction
- from front side
  in forward direction
- from front side
  in backward direction
Which is the dominant “channel” for given conditions?

---
Fast ions seen in PIC simulations suggest
several possible mechanisms of ion acceleration
1D PIC simulation
I=3.5×1020W/cm2 ,
ne=1022cm-3
Three fast ion populations,
accelerated
- from rear side
  in forward direction
- from front side
  in forward direction
- from front side
  in backward direction
Which is the dominant “channel” for given conditions?

---
Fast ions seen in PIC simulations suggest
several possible mechanisms of ion acceleration
1D PIC simulation
I=3.5×1020W/cm2 ,
ne=1022cm-3
Three fast ion populations,
accelerated
- from rear side
  in forward direction
- from front side
  in forward direction
- from front side
  in backward direction
Which is the dominant “channel” for given conditions?

---
The “front vs rear side” debate
Clark et al: “It is likely that the protons originate from the front surface of the target and are bent by large magnetic fields which exist in the target interior.”
Maksimchuk et al: “The protons [...] appear to originate from impurities on the front side of the target [...] The maximum proton energy can be explained by the charge-separation electrostatic-field acceleration due to vacuum heating.
Snavely et al: “We have
concluded that light pressure effects at the front surface
focal spot on the target could
not generate the observed
ions because of the clear
evidence that the protons are
emitted perpendicular to the
rear surface(s) of the target.”

---
The Target Normal Sheath Acceleration
model of proton acceleration
Physical mechanism:
acceleration in the space-charge
electric field generated by
“fast” electrons
escaping from the target
[S. Wilks et al, Phys. Plasmas 8 (2001) 542]

---
Modeling of sheath acceleration:
the problem of plasma expansion in vacuum
Analytical approach:
- electrostatic approximation
- fluid ions
- electrons in Boltzmann
  equilibrium
- “fast” electron temperature
    and density as input
    parameters
“Mora's formula” from
isothermal, semi-infinite
slab model
[P.Mora, PRL 90 (2003) 185002]
- diverges with time (infinite
energy available!)
- “corrected” assuming
finite acceleration time tp
[J.Fuchs et al, Nature Phys. 2 (2005) 48]

---
Modeling of sheath acceleration:
the problem of plasma expansion in vacuum
Analytical approach:
- electrostatic approximation
- fluid ions
- electrons in Boltzmann
  equilibrium
- “fast” electron temperature
   and density as input
   parameters
- thin slab to account
  for finite energy
Comparison with
numerical PIC
results (including
kinetic effects):
S.Betti, F.Ceccherini, F.Cornolti, F.Pegoraro, Plasma Phys. Control. Fusion 47 (2005) 521
F.Ceccherini, S.Betti, F.Cornolti, F.Pegoraro, Laser Physics 16 (2006) 1

---
How to diagnose the electric fields directly?
Idea: use the protons as a probe
Due to high laminarity
the proton beam has
imaging properties
The short duration of
the proton burst allows
picosecond
temporal resolution
Protons of a given energy
will cross the probed object
at a particular time.
An energy-resolving detector
(e.g. Radiochromic Film)
thus provides
multiframe capability
Borghesi et al, Phys.Plasmas 9 (2002) 2214
Borghesi et al, Phys.Rev.Lett. 92 (2004) 055003
Cowan et al, Phys.Rev.Lett. 92 (2004) 204851
In a laser-plasma experiment
the proton probe is easily
synchronized with the interaction

---
Experimental detection of sheath fields
using the proton diagnostic
Expanding, bell-shaped
electric field front
observed in proton
images and
deflectograms
L. Romagnani, J. Fuchs, M. Borghesi, P. Antici, P. Audebert, F. Ceccherini, T. Cowan,
T. Grismayer, S. Kar, A. Macchi, P. Mora, G. Pretzler, A. Schiavi, T. Toncian, O. Willi,
Phys. Rev. Lett. 95 (2005) 195001

---
Experimental detection of sheath fields
using the proton diagnostic
Experimental results
have been compared
with PIC simulations
using the plasma
expansion model.
Particle tracing
simulations of proton
deflection in the PIC
fields (plus an “heuristic”
modeling of the 2D
expansion) fit well
experimental images
and deflectrograms
Comparison of fluid
and kinetic (PIC) results
show the importance
of kinetic and
non-thermal effects in
the plasma expansion
L. Romagnani, J. Fuchs, M. Borghesi, P. Antici, P. Audebert, F. Ceccherini, T. Cowan,
T. Grismayer, S. Kar, A. Macchi, P. Mora, G. Pretzler, A. Schiavi, T. Toncian, O. Willi,
Phys. Rev. Lett. 95 (2005) 195001

---
        Experimental State of the Art (quick look)
Scaling of ion energy
and number
vs. pulse duration and irradiance checked vs.”modified” Mora's isothermal model
From:	M.Borghesi et al, Fusion Science & Technology 49 (2006) 412;
J. Fuchs et al, Nature Physics 2 (2005) 48 .
A few recent results, all based on TNSA:
- narrow energy spectrum of protons from engineered double-layer target
[H. Schwoerer et al, Nature 439 (2006) 445]
- MeV carbon ions from pre-heated (“decontaminated”) target
[B. Hegelich et al, Nature 439 (2006) 441]
- Ultrafast “laser-plasma microlens” for ion beam focusing
  and energy selection
[T. Toncian et al, Science 312 (2006) 410]

---
What about other ion populations?
For prepulse-free measurement, the density profile is sharp
also at the front side: TNSA in backward direction observed
for thin targets (electrons have time to reflux back)
T.Ceccotti et al, PRL 99 (2007) 185002

---
What about other ion populations?
For prepulse-free measurement, the density profile is sharp
also at the front side: TNSA in backward direction observed
for thin targets (electrons have time to reflux back)
T.Ceccotti et al, PRL 99 (2007) 185002
In petawatt (I~1020 W/cm2)
experiments for “quite thin”
targets a highly collimated
dense plasma jet from the
rear side is observed:
due to front side ions?
(absence of jet for larger thickness ascribed to
collisional ion stopping in the target)
S.Kar, M.Borghesi, S. V. Bulanov, A.J.MacKinnon, P.K.Patel, M.Key, L.Romagnani,
A.Schiavi, A.Macchi, O.Willi,
RAL CLF annual report 2003-2004, p.24,
submitted to PRL

---
Simulations suggest regime transition
at intensities ~ 1021 W/cm2
Results from “multi-parametric” PIC simulations:
- for maximal ion energy an
  optimal areal density ned exists
  for given intensity I
- ion energy scales with laser energy eL
    as eL1/2 for I<1021 W/cm2
  as eL for I>1021 W/cm2
- transition is explained by
  the dominance of
  Radiation Pressure Acceleration
T.Esirkepov et al, PRL 96 (2006) 105001

---
Relativistic ions: the “Laser-Piston” regime
Ultra-relativistic interaction regime
“dominated by radiation pressure”
T.Esirkepov, M.Borghesi, S.V.Bulanov,
G.Mourou, T.Tajima, PRL 92, 175003 (2004)
Required laser intensity
I≥1023 W/cm2
The foreseen ion beam parameters
make this attractive as a driver of
low-energy neutrino sources
for studies of CP violation
in e oscillations
S.V.Bulanov, T.Esirkepov, P.Migliozzi, F.Pegoraro,
T.Tajima, F.Terranova, NIM A 540, 133 (2005);
F. Terranova, S.V.Bulanov, J.L.Collier, H.Kiriyama,
F.Pegoraro, NIM A 558, 430 (2006).

---
Old motivations for Radiation Pressure Acceleration
Analysis based on relativity and a rigid mirror acceleration
model suggests 100% efficiency as V®c

---
Maximize the effect of Radiation Pressure:
the “optical mill” (Solar radiometer) example
The mill spins in
the opposite direction
to what we'd expect
thinking of Prad only:
the heating of the
black (absorbing)
surface increased
the thermal pressure
of the background gas
(imperfect vacuum!)
In the high-intensity irradiation of a solid-density (plasma)
target, “heating” is due to energy absorption into electrons

---
        How to “switch off” fast electrons
Forced oscillations of the electrons
across the plasma-vacuum interface
(L << l) driven by the 2w component
of the JxB force (normal incidence) are
non-adiabatic and lead to
electron acceleration
 S. Tuveri, tesi di Laurea, 2006

---
        How to “switch off” fast electrons
For circular polarization,
 the 2w component of the JxB
force vanishes:
- inhibition of electron acceleration
- “direct” ion acceleration
(i.e. “dominance” of
Radiation Pressure)
A.Macchi, F.Cattani, T.V.Liseikina, F. Cornolti,
Phys.Rev.Lett 94, 165003 (2005)
 S. Tuveri, tesi di Laurea, 2006

---
Features of Ion Acceleration with Circular Polarization
[Macchi et al, PRL 94 (2005) 165003;
Liseikina and Macchi, APL 91 (2007) 171502]
1D and 2D PIC simulations,
“thick” targets
I=1018-1021 W/cm2 ,
t=10-100 fs
Features at
I=3.5×1020W/cm2 , ne=1022cm-3
efficiency=14%
angular spread< 5 deg.
mean energy=10 MeV
energy spread 20%
production of a
single ultrashort ion bunch
possible with shorter pulses

---
Features of Ion Acceleration with Circular Polarization
[Macchi et al, PRL 94 (2005) 165003;
Liseikina and Macchi, APL 91 (2007) 171502]
1D and 2D PIC simulations,
“thick” targets
I=1018-1021 W/cm2 ,
t=10-100 fs
Features at
I=3.5×1020W/cm2 , ne=1022cm-3
efficiency=14%
angular spread< 5 deg.
mean energy=10 MeV
energy spread 20%
production of a
single ultrashort ion bunch
possible with shorter pulses

---
Features of Ion Acceleration with Circular Polarization
[Macchi et al, PRL 94 (2005) 165003;
Liseikina and Macchi, APL 91 (2007) 171502]
1D and 2D PIC simulations,
“thick” targets
I=1018-1021 W/cm2 ,
t=10-100 fs
The “Xmas tree” is a
contour plot of ion energy
vs. emission angle,
showing a high and
energy-dependent
collimation
(submitted to IEEE - Images in Plasma Science)
Features at
I=3.5×1020W/cm2 , ne=1022cm-3
efficiency=14%
angular spread< 5 deg.
mean energy=10 MeV
energy spread 20%
production of a
single ultrashort ion bunch
possible with shorter pulses

---
An application of circularly polarized LIA
Driver of beam fusion
reactions in D or DT
targets for a proposed
scheme of a
femtosecond source
of MeV neutrons
[A. Macchi,
Appl.Phys.B 82, 337 (2006)]
A source for
ultrafast control
of nuclear processes
and
time-resolved
spectroscopy of nuclei?

---
RPA of a thin foil
- For target thickness d<ui tp “repeated” or “multi-staged” RPA
  of all the target ions occurs.
- Circular polarization plus ultrathin targets (plus ultrahigh contrast?)
  is promising for high energy (GeV) with intensities ~1021 W/cm2
[X.Zhang et al, Phys. Plasmas 14 (2007) 073101;
 A.P.L.Robinson et al, arXiv:0708.2040;
 O. Klimo et al, submitted to Phys. Rev. E]
- In this regime the ion energy scales with pulse duration tp
  at given intensity

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic peak amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case

---
Simulation of thin foil RPA with FLAME parameters
- Carbon target, thickness d=0.04mm, ne=250nc=4.3×1023 cm-3
- Laser: 26 fs pulse, average intensity I=1.8×1020 W/cm2
relativistic amplitude a0 = 13
- comparison of Linear Polarization vs Circular Polarization case
similarity of spectra suggest relatively weak differences between CP and LP:
- RPA already dominant?
- optimal thicknesses for acceleration?
- Regime may be quite different with preplasma (thicker targets)

---
Conclusions
- So far experiments on ion (proton) acceleration from solid
  targets are dominated by the TNSA mechanism
- Present regimes may approach the transition to the
  Radiation Pressure Acceleration regimes
- Use of circular polarization enforces the RPA dominance
- Proof of principle of RPA on thin foils may be obtained in
   present-day laser facilities, including FLAME
This talk may be downloaded from
www.df.unipi.it/~macchi/talks.html

---
        Basis of theoretical and numerical modeling
“Plasma physics is just waiting for bigger computers”
Vlasov-Maxwell
system for
collisionless,
classical plasmas:
kinetic equations are
coupled to EM fields
Mostly used numerical approach: particle-in-cell (PIC) method
[Birdsall & Langdon, Plasma Physics via Computer Simulation (IOP, 1991)]
3D numerical simulations of “realistic” experimental conditions
is most of the times beyond present-day supercomputing power
Models are needed to interpretate experiments and unfold the
underlying physics